## Slide 1
Design and status of a near-infrared multi-object spectrograph for the TAO 6.5-m Telescope
Masahiro Konishia < konishi@ioa.s.u-tokyo.ac.jp >
Kentaro Motoharaa, Mamoru Doia, Shigeyuki Sakoa, Koji Toshikawaa, Natsuko Mitania, Tsutomu Aokib,
Toshihiro Handaa, Yoshifusa Itac,d, Daisuke Katoe,f, Kimiaki Kawaraa, Kotaro Kohnoa, Shintaro Koshidaa, Takeo Minezakia,
Takashi Miyataa, Takao Soyanob, Toshihiko Tanabea, Masuo Tanakaa, Ken’ichi Tarusawab, and Yuzuru Yoshiia
7735-252
      aInstitute of Astronomy, the University of Tokyo, Mitaka, Japan; bKiso Observatory, Institute of Astronomy, the University of Tokyo, Kiso, Japan;
      cNational Astronomical Observatory of Japan, Mitaka, Japan; dAstronomical Institute, Tohoku University, Sendai, Japan;
      eDepartment of Astronomy, the University of Tokyo, Tokyo, Japan; fInstitute of Space and Astronautical Science, Sagamihara, Japan
References
[1] Yoshii, Y. et al., “Tokyo Atacama Observatory Project,” Proc. of the IAU 8th Asian-Pacific Regional Meeting II, 35–36 (2002).
[2] Yoshii, Y. et al., “The University of Tokyo Atacama Observatory 6.5m Telescope project,” Proc. SPIE, in this conference (2010).
[3] Miyata, T., et al., “Site evaluations of the summit of Co. Chajnantor for infrared observations,” Proc. SPIE 7012, 701243–701243–8 (2008).
[4] Motohara, K. et al., “Seeing environment at a 5640m altitude of Co. Chajnantor in northern Chile,” Proc. SPIE 7012, 701244–701244–10 (2008).
[5] Suzuki, R. et al., “Multi-Object Infrared Camera and Spectrograph (MOIRCS) for the Subaru Telescope I. Imaging,” PASJ 60, 1347–1362 (2008).
[6] Tokoku, C. et al., “Infrared multi-object spectrograph of MOIRCS,” Proc. SPIE 6269, 62694N (2006).
2. Specification of SWIMS
4. Multi-Object Slit Unit
5. Schedule
Figure2. Observed-frame wavelength of optical emission lines as a function of redshift. Red and green hatched regions represent wavelength ranges with low atmospheric transmittance (<50%) at the TAO site and the VLT site, respectively. Solid lines show the wavelength of Hα (λrest = 6563Å), [OIII] (λrest = 4959, 5007Å), Hβ (λrest = 4861Å), and [OII] (λrest = 3727Å). Wavelength coverages of SWIMS are also shown with arrows on the right.
1. TAO PROJECT & NIR ASTRONOMY
Figure 1. Atmospheric transmittances in NIR wavelengths at the TAO site (Co. Chajnantor, 5,600m alt., PWV=0.5mm) and the VLT site (Co. Paranal, 2,600m alt., PWV=6.0mm) calculated using ATRAN software (Lord, S.D. 1992, NASA).
*PWV: Precipitable Water Vapor
The University of Tokyo Atacama Observatory (TAO) is a project to construct a 6.5m infrared-optimized telescope at the summit of Co. Chajnantor (5,640m altitude) in Atacama Desert, Chile (PI: Yuzuru Yoshii)1,2. Thanks to the dry climate and high altitude3,4 at the TAO site, high atmospheric transmittance is expected in near-infrared (NIR) wavelengths (Figure 1), which is suitable for redshift surveys of distant astronomical objects (galaxies, galaxy clusters, and so on).
Figure 3. 3D (left) and 2D cross-sectional (right) schematics of SWIMS. Dimension and weight of SWIMS are ~2x2x2 m3 and 2t .(Designed by Sumitomo Heavy Industries, Inc)
Cryogenic cooler
Focal plane dewar
Mask dewar
Main dewar
Pre-cooling line
The most remarkable feature of SWIMS is NIR two-band simultaneous (imaging or MOS) observations (0.9-1.4 and 1.4-2.5 μm) using a dichroic mirror.
3. Optics
Figure 4. Optical design of SWIMS. (Designed by Optcraft)
The SWIMS optics is currently optimized for the Subaru Telescope (Figure 4 and Table 2).
A dichroic mirror is placed in the collimated beam for simultaneous-color observations. All of the components are placed on a optical bench (1400 x 920mm), and cooled down below 90K. Expected performances are shown in Figure 5. Good image qualities are achieved, and image distortions are negligible across the FoV.
By July 2010 | Detailed designs of optics, mechanics and MOS to be completed.
2011 | Dewar, MOS and detectors to be delivered.
2012 | Installation and assembly of the components to be completed.
2013 | Transported to Subaru, and First Light.
 Part of the initial design of the instrument is optimized for the Subaru.
Camera Units:
Two channels: optimized for λ=0.9-1.5 μm (blue) and λ=1.4-2.5 μm (red)
Collimator Unit:
Currently optimized for the Subaru Telescope
Re-optimized by replacing the first three lenses when mounted on the TAO
Field lens : ϕ216mm, CaF2
Table2. Specifications of the optics.
Figure 5. Left: Spot diagrams for 6’.6 x 6’.6 FoV of the imaging mode. Red, green, blue spots correspond to λ = (0.9, 1.25, 1.50) μm, and (1.4, 1.8, 2.4) μm for the blue
Blue
Red
We are planning to carry out commissioning and early science observations on the Subaru Telescope at Hawaii before the construction of the TAO 6.5m telescope.
The full FoV at the Nasmyth focus of the TAO 6.5m telescope (ϕ9’.6) is covered by four HAWAII-2RG arrays with 0”.13 pixel-1 sampling. During the commissioning phase on the Subaru, two arrays are installed on each channel, which covers 6’.8 x 3’.4 with 0”.10 pixel-1.
Table1. Specifications of SWIMS.
(Nasmyth)
(Cassegrain)
A NIR spectrograph for the TAO 6.5m telescope, SWIMS (Simultaneous-color Wide-field Infrared Multi-object Spectrograph), has capabilities of wide-field imaging and multi-object spectroscopy (MOS) for a wide spectral range from 0.9-2.5 μm at a time using a dichroic mirror placed in the collimated beam. Taking advantages of the site, SWIMS enables us to obtain various redshifted spectral features (emission lines and continuum breaks) simultaneously under same observational conditions (weather, telescope, and the instrument), as shown in Figure 2.
The design of the MOS unit of SWIMS is based on MOIRCS5,6 on the Subaru Telescope,
Mask storage dewar
Robotic mask catcher
20 slit masks are stored in a carousel
GM cryo-cooler equipped.
and refined to be operative at the Nasmyth focus of the TAO 6.5m telescope.
Neodymium magnets are used to hold a slit mask on the focal plane as well as to stock the mask at the carousel.
A slit mask holder is designed to hold a cylindrically curved mask sheet to compensate for the curved focal plane of the telescopes, especially for the TAO 6.5m telescope.
Figure 6. 3D schematic view of the MOS unit. (Designed by Sentencia Corporation )
Mask Holder
Mask Sheet
Fixture Ring
Neodymium magnets at each corner
Figure 7. Left: A schematic drawing of the slit mask. A mask is made of aluminum sheet, and its shape is a combination of a circle with 210mm in diameter and a rectangle with 150mm x 210mm. Right: A prototype mask holder.
Detectors:
HAWAII-2RG array with 2.5 μm cutoff
SIDECAR ASICs for readout
Two arrays cover 6’.8 x 3’.4 with 0”.10 pixel-1
and red channels, respectively. The box is 5.4 pixels (0”.53) on a side. Middle: Distortion maps for 6’.6 x 6’.6 FoV of the imaging mode (exaggerated by a factor of 50). Right: spot diagrams of the spectroscopy mode. The box is 5.4 pixels (0”.53) on a side.
Blue
Red
Figure 8. Mask storage dewar and Carousel.