## Slide 1: Status of SWIMS and MIMIZUKU: New Infrared Instruments for TAO 6.5m Telescope
K. Motohara, T. Aoki, K. Asano, M. Doi, T. Handa, N. Mitani Kato,
K. Kawara, K. Kohno, M. Konishi, S. Koshida, T. Minezaki, T. Miyata, T. Morokuma, T. Nakamura, S. Sako, T. Soyano, Y. Tamura, M. Tanaka, T. Tanabe, K. Tateuchi, K. Tarusawa, M. Uchiyama, and Y. Yoshii (Univ. Tokyo)

## Slide 2: お願い
光赤天連運営委員選挙してます
  今週末締切！
  まだ１６人からしか投票がありません！
  今すぐ投票を！
光赤天連会費徴収してます
  今週いっぱい、現金徴収
  あるいは郵便振替で
  \1k/yr
天文学会秋季総会の事前投票を！
  天文月報の折り込みハガキで
  月曜日時点で２０２票（まだ足りない！）

## Slide 3: Instrumentation for TAO 6.5m
２つの観測装置
  NIR MOS spectrograph/Imager (SWIMS)
  MIR Imager/Spectrograph (MIMIZUKU)
２００９年度補正予算で製作費用が措置された。 （～２０１０年度）

## Slide 4: NIR Camera : SWIMS
Simultaneous-band Wide field Infrared MOS Spectrograph
  広い視野: 9.6’ Φ with 4kx4k pixels
  ２バンド同時撮像分光
    blue channel : 0.9-1.4um
    red channel : 1.5-2.5um
  多天体分光
    with cooled multi-slit masks
    max. 30 objects
    0.9-2.5mm simultaneous spectroscopy (R~1000)
  IFU module 検討中
  Member : 本原、小西、高橋、 舘内、加藤
2.0m

## Slide 5: 0.9-2.5m同時撮像分光
Telescope Focal Plane
Collimator Optics
Blue Channel
Red Channel
Focal Plane
Focal Plane
Dichroic Mirror
ダイクロイックミラーで1.4umで分割して同時観測
  Spectroscopy from 0.9-2.5um with R~1000(0.6”slit)
    正確な輝線比
  Dual-band wide-field imaging
    高い観測効率
各焦点に４個のHAWAII-2RGs (今はまだ 2個)

## Slide 6: Science with SWIMS Galaxy Redshift Surevey
TAOサイトでは近赤外線の大気の窓がつながる : Ideal for the redshift survey @ z=1-2.5
0.9-2.5mm のスペクトルを一度に取得 : precise continuum / line ratio measurement possible
複数輝線の同時狭帯域撮像が可能 (e.g. Ha/OIII, Hb/OII)

## Slide 7: Science with SWIMS New Window for Paa
水素 Paa line (1.8751mm) の観測が可能となる
  Strongest Hydrogen Line in NIR
  Good probe in dusty environment
Starburst Galaxies IC4686/4687
舘内ポスター参照

## Slide 8: サイエンス検討ワークショップ
2009/9/11
32名参加
幅広いサイエンス
  太陽系
  YSO食連星
  ミラ型変光星
  近赤外線超新星
  遠方銀河探査
  遠方銀河団・原始銀河団サーベイ
  サブミリ銀河フォローアップ
  QSO
  AGN変光
  AKARI/SPICAとの連携

## Slide 9: SWIMS Manufacturing Underway
2m
MOS Exchanger (Sentencia)
Main Dewar /Cooler(SHI)
HAWAII-2RGs (Teledyne)
Grism (Optcraft / Richardson)
Aspherical ZnSe Lenses
(Optcraft / II-IV)

## Slide 10
Assembly Test at Mitaka New Building (2011/6)

## Slide 11: Mask Catcher Unit

## Slide 12: Mid-infrared Instrument MIMIZUKU
Mid Infrared Multi-mode Imager for gaZing at the Unkown Universe
  中間赤外線観測装置
  広い波長範囲をカバー
    NIR channel : 2um – 5.6um (InSb)
    MIR-S channel : 6 – 26um (Si:As)
    MIR-L channel : 24 – 38um (Si:Sb)
  高い空間分解能
    >6umで回折限界を達成
    1.2 arcsec @ 30um
  相対測光による変光天体検出
  Member : 宮田、酒向、上塚、 中村、浅野、内山

## Slide 13: MIMIZUKU Wide Wavelength Coverage + High Spatial Resolution
30um帯で1arcsecの
解像度を達成！
wavelength (um)
10
20
30
40
Spatial resolution (arcsec)
10.0
0.1
1.0
SPITZER
SOFIA
SUBARU
SPICA
JWST
AKARI
TAO/
MIMIZUKU
30m telescopes
50

## Slide 14: MIMIZUKU Accurate Monitoring w/ Field Stacker
視野合成▽鏡
低温光学系に
ピックアップ鏡
ピックアップ鏡
回転テーブル
その上にXステージ
望遠鏡の像（仮想的）
1’x2’
1’x2’
2’x2’
2つの視野をpickupすることで
MIRで視野内相対測光を実現
従来に比べて格段に精度のよい
時間変動のモニタリングが可能
Evolved stars
Supernovae/Novae
YSO disks…

## Slide 15: Science with MIMIZUKU
原始太陽系円盤
でのダスト進化
大質量星、晩期型星
でのダスト生成
太陽系内天体での
ダスト生成
大質量星形成
遠赤外線ソース
の高解像度観測
赤外線ダーククラウド
30μm帯
の開拓
系統的
モニタ観測
高感度20μm帯
観測

## Slide 16: サイエンス検討ワークショップ
2009/7/24
34名参加
多くのサイエンス
  変光星分光撮像モニター
  銀河中心のミラ型変光星
  分子光球
  大質量星形成
  太陽系小天体、彗星
  惑星磁気圏
  CDMサブハロ質量測定
  Dusty AGN
  ALMA/ASteとの連携

## Slide 17: MIMIZUKU Manufacturing Underway
Field Stacker Unit
CVD diamond
window
(φ70mm)
Si grism
Mesh filter
for 30um
Cold Optics

## Slide 18
Delivered Dewar Jacket to Mitaka New Building (2011/6)

## Slide 19: SWIMS / MIMIZUKU on Subaru
TAO 6.5m not available before 2016
First science with Subaru (2013 or 2014?)
Will be Opened as PI Instruments
SWIMS
  Collimator design optimized for Subaru (Re-optimized to TAO by changing the collimator unit)
  FoV of 6.6’ x 3.3’ (MOIRCS : 7’x4’)
  0.10”/pix
MIMIZUKU
  NIR / MIR-S channels can be used at Subaru
  Monitoring capability

## Slide 20: Summary
TAO 6.5m望遠鏡の２観測装置を開発している
  SWIMS(NIR)
  MIMIZUKU(MIR)
2013年を目標にすばるでのサイエンス観測を始めたい
  PI共同利用へ供する予定
サイエンス検討を進めている
興味のある方はぜひご連絡を！

## Slide 22: Schedule
Items | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
6.5-m telescope Detailed design Primary Enclosure, telescope structure Road and ground activities Enclosure installation 6.5-m telescope installation 6.5-m telescope operation |  |  |  |  |  |  |  |  | 
1st generation instruments Detailed design Assemble, laboratory tests test observations at Subaru Observations at TAO 6.5m |  |  |  |  |  |  |  |  | 
?? TBD ??

## Slide 23: Advantage of Co. Chajnantor
Photometric nights > 60%, / usable >80% (Miyata+08)
Median Seeing 0.7”台 @ Ks-band
高地 (5640m/<0.5atm) で観測している (PWV 0.5mm) ため、高い赤外線透過率
Excellent observational condition in
both NIR(1-2.5mm) and MIR (5-40mm)
Atmospheric
Transmittance

## Slide 24: TAO 6.5m Telescope
最も赤外線観測に適した望遠鏡
望遠鏡の
  最終F
  カセグレンインターフェース
はすばると同じ。
⇒すばると観測装置を共有できる
Telescope type : Cassegrain / Ritchey-Chretien
Primary diameter : 6,500 mm
Final focal ratio : 12.2
Foci : Cassegrain + 2 Nasmyth
Field of view : φ25 arcmin

## Slide 25: MIMIZUKU Science Targets
The highest spatial resolution at 30um ⇒ Useful for detailed studies of proto-planetary / debris disk and dust shells
wavelength (um)
10
20
30
40
Spatial resolution (arcsec)
10.0
0.1
1.0
SPITZER
SOFIA
SUBARU
SPICA
JWST
AKARI
TAO
30m
50
30um
150K-30K region

## Slide 26: MIR : MIMIZUKU
Mid-Infrared Multi-field Imager for gaZing at the UnKnown Universe
  PI : Takashi Miyata
  Wide wavelength coverage
    InSb channel : 2-5.6um
    Si:As channel : 6-26um
    Si:Sb channel : 25-38um
  Diffraction limited spatial resolution
    0.4 arcsec @ 10 micron
    0.8 arcsec @ 20 micron
    1.2 arcsec @ 30 micron
  Accurate monitoring
    simultaneous observations of two discrete fields
  Member : 宮田、酒向、上塚、 中村、浅野、内山

## Slide 27: Accurate Photometry in MIR
Field Stacker Unit
Simultaneously observe two objects for diffferential photometry
~50% of 9/18um sources have a counterpart star
Triangle Prism Shape Mirror
to Cold Optics
Pick-up mirror
Pick-up mirror
Rotatable Table
Telescope Field of View
1’x2’
1’x2’
2’x2’
Telescope | FOV of telescope | 9 micron |  | 18 micron | 
 |  | > 50mJy | >300mJy | >130mJy | >1Jy
TAO | 25’ | 55 % | 51% | 51 % | 15%
Subaru | 5’ | 51% | 10% | 41% | 0.3 %

## Slide 28: Performance of Optics (Subaru Design)
Blue Channel
Red Channel

## Slide 29: Focal Plane Arrays
8 HAWAII2 RGs / 2.5mm cutoff => Currently only 4 procured/delivered
SIDECAR ASICs for readout
Covers central 6.6’x3.3’ FoV@Subaru
0.1”/pix sampling
#196
#206
#208
#191
Dark Current < 0.005e-/s

## Slide 30: MOS Slit Plate Exchanger (Design/Fabrication : Sentencia)
Mask Catcher Unit (Robo-hand)
Not Shown here
Gate Valve
Collimator Unit
MOS Slit Masks
Based on the design of MOIRCS
  Turret-type mask stocker
  Robotic mask exchanger
~2.3m

## Slide 31: MOS Slit Unit / Holder
Maximum # of mask slit : 20
New design with high reliability
  Magnet – latch (Both at the focus and the stock)
  Operative even at the TAO Nasmyth focus
  Curved mask to adjust focal plane curvature
Prototype Mask Holder
250mm
210mm
Neodyium Magnets

## Slide 32: Schedule
2010/Nov : Array #1, #2 delivery
2011/Jan : Closing design phase
2011/Jan : Array #3, #4 delivery
2011/Jan : Dichroic mirror delivery
2011/Mar : Completion of a new laboratory building
2011/Mar: Delivery of the dewar, MOS, optics componetns
2011/Q2-2012/Q2 : Assembly, adjustment, etc…
2012/Q3 or later : Transport to Subaru, setup
2013/Q1 : First Light at Subaru ?

## Slide 33: New Building at Mitaka
Wii be completed in mid-March

## Slide 35: Atmospheric Transmittance
5600m
PWV=0.5mm
4200m
PWV=1.0mm
2600m
PWV=6.0mm

## Slide 36: Dichroic Mirror