## Slide 1: miniTAO/MAX38 Summary Report
T. Kamizuka (IoA/UT)
miniTAO/MAX38 team
miniTAO team

## Slide 2: miniTAO/MAX38
MAX38 = Mid-infrared Astronomical eXplorer
Mid-infrared instrument on miniTAO
Imaging and Spectroscopy
30-micron band imaging
Atmospheric Transmittance at 4200/5600m altitude
miniTAO/MAX38
30-μm band open!
Explore it !

## Slide 3: miniTAO/MAX38
Specifications
Imaging
  (L’, ) N, Q, 30μm-bands
  Diffraction limited imaging (λ>8.9 μm)
N-band Spectroscopy
  λ= 7.2-12.7 μm
  Low-res. grism spc. (R~50)
※Details available in Asano + 2012
and MAX38 HP
Detector | Si:Sb BIB MF-128 (DRS)
Format | 128 x 128 (Img: 64x128)
FoV | 1.3 arcmin x 2.5 arcmin
Pixel Scale | 1.26 arcsec/pix
Filter name | Wave-length (μm) | Band-width (μm) | 1σ1s Sensitivity (Jy) | Spatial Resol. (asec)
8.9μm | 8.9 | 0.77 | 1.7 | 2.4
9.8μm | 9.8 | 0.91 | 2.8 | 2.7
12.2μm | 12.2 | 0.75 | 3.1 | 3.2
18.7μm | 18.7 | 0.9 | 2.2 | 4.9
24.7μm | 24.7 | 2.0 | ? | ?
MMF-31 | 31.7 | 2.2 | 28 | 7.6
MMF-37 | 37.3 | 2.4 | 70 | 8.5
Detector Specifications
MIR-band imaging properties

## Slide 4: Operation History
Operation team
  Miyata-Lab. member &
  TAO member
First Light: 2009/11
Science Observations
2009/11, 2010/9-10,
2011/5, 2011/10-11,
2012/10
~280h observations
Struggling against machine troubles and bad weather…
Galactic center 31μm-image
Miyata-san and Asano-san installing MAX38
Snow storm at Chajnantor

## Slide 5: Observation Programs
30-micron Imaging
Luminous blue variables (Nakamura-san)
Planetary nebulae (Asano-san)
Massive star forming regions (Uchiyama-san)
N-band Imaging
Volcano on Io (Yoneda-san)
Asymptotic Giant Stars (Kamizuka)
Asteroid (Miyata-san)
N-band Spectroscopy
Earth atmosphere (Hayashi-san)
LBV η Car
PN Mz3
Io

## Slide 6: Asteroid
MIR Light Curve obtained by MAX38
Asteroid 2005 YU55
Near earth asteroid
Close Earth-approach on 2011/11/08
  ～0.85 lunar distance
Detailed observations in many wavelengths
MAX38 got thermal infrared data
temperature variation
thermal inertia
Observations + Thermo-Physical-Model
High thermal inertia
= Rubble-pile asteroid like Itokawa ?
Paper is coming soon
Moving asteroid on MAX38 image
Itokawa taken by Hayabusa
5sec
7sec

## Slide 7: Asymptotic Giant Branch Stars
AGB Stars
Dying low/intermediate-mass stars
Dust forming from ejected materials
Good targets to probe dust formation
Objects restarted dust formation
Dust forming region observable directly
Dust formation can be detected easily
Search with MAX38
One object, T Col, shows clear spectral change (10 targets observed)
T Col possibly restarted dust formation
in last 20-30 years
Mass-loss and dust formation
around AGB star
MIR spectrum of T Col

## Slide 8: Future Plan
Completion of MIMIZUKU required
Operation of MIMIZUKU@Subaru needed
  MIMIZUKU = MIR instrument for TAO
Parallel operation is difficult
MAX38 will/may be closed in late 2013
Your strong request or help may extend the MAX38 life.
Please give your opinion at the night session etc.
MIMIZUKU
Current schedule plan

## Slide 9: Summary
MAX38 has been conducted about 280h observations since 2009/11.
Many kind of objects are observed.
Dust formation around dying stars
Star forming regions
Solar system objects
Earth atmosphere
Many presentations in this workshop
MAX38 will be closed in late 2013.
Please give your comments on this.